## Slide 1: IPP Reprint Password Use Cases
The Printer Working Group
®
Smith Kennedy, HP Inc.
PWG August 2018 Face-to-Face
August 15, 2018

## Slide 2: Review Concepts and Terminology

## Slide 3: Terminology
Job Instructions [PWG 5100.11]
  Information that affects how the job and its associated documents are to be processed
    Job Template Attributes
    Some Operation Request Attributes
    Other attributes (such as defaults) that are applied to a Job
Job Submission Operations [PWG 5100.11]
  IPP operations that create jobs and send document content
    Print-Job
    Print-URI
    Create-Job
    Send-Document
    Send-URI

## Slide 4: Terminology
Retained Job [PWG 5100.11]
  A Job that the Printer retains in the Job Retention Phase1 after processing it, for an implementation-defined period (including zero seconds) or removed by an explicit Delete-Job or Purge-Jobs operation
  An exact copy of a Retained Job can be processed using a Reprocess-Job2 operation.
  A modified copy of a Retained Job can be processed using a Resubmit-Job operation.
Saved Job [PWG 5100.11]
  A Saved Job is a Retained Job that the Printer retains indefinitely (until removed by a Delete-Job or Purge-Jobs2 operation) so that a copy of it can be reprinted any time using the Reprocess-Job2 or Resubmit-Job operations, rather than aging the job out after an implementation-defined period.
1 See [RFC8011] section 5.3.7.2 Partitioning of Job States
2 Deprecated

## Slide 5: Operations and Attributes
"job-password" [PWG 5100.11]
  Information that affects how the job and its associated documents are to be processed. This includes the Job Template Attributes, some Operation Request Attributes, and other attributes (such as defaults) that are applied to a job.
Job Submission Operations [PWG 5100.11]
  The Job-Submission Operations are the IPP operations that create jobs and send document content, namely Print-Job, Print-URI, Create-Job, Send- Document and Send-URI. See [RFC8011] for further information.
Retained Job [PWG 5100.11]
  A Retained Job is a job that the Printer retains in the so-called Job Retention Phase (see [RFC8011] section 5.3.7.2 Partitioning of Job States) in the job’s terminal state (‘completed’, ‘aborted’, or ‘canceled’) after processing it, for an implementation-defined period (including zero seconds) or removed by an explicit Delete-Job or Purge-Jobs operation. An exact copy of a Retained Job can be processed using a Reprocess-Job operation. A modified copy of a Retained Job can be processed using a Resubmit-Job operation.
Saved Job [PWG 5100.11]
  A Saved Job is a Retained Job that the Printer retains indefinitely (until removed by a Delete-Job or Purge-Jobs operation) so that a copy of it can be reprinted any time using the Reprocess-Job or Resubmit-Job operations, rather than aging the job out after an implementation-defined period.

## Slide 6: Common Supported Use Cases

## Slide 7: Use Case Review
U1: Job Submitted to Print
U2: Job Submitted with Job Password
  "job-password"  no job processing until password provided
U3: Job Submitted as a Saved Job
  "job-save"  job processing causes job to be saved
U4: Print a Saved Job via IPP Resubmit-Job
  Reprint caused by Client IPP operation
U5: Print a Saved Job via Control Console
  Reprint caused by direct user interaction with printer (no IPP)

## Slide 8: U1: Job Submitted to Print
Client
Printer
Process Job
Job Creation operation
Job
A
Print
Engine
Control Console
Storage

## Slide 9: U2: Job Submitted with Job Password
Printer
Process Job
Touch, etc. to
enter job password
Wait for password
password
Client
Job Creation operation
with "job-password"
Job
A
Print
Engine
Control Console
Storage

## Slide 10: U3: Job Submitted as a Saved Job
Printer
Storage
Process Job
Client
Job Creation operation
with "job-save"
Job
A
Job
A
Print
Engine
Control Console

## Slide 11: U4: Print a Saved Job via IPP Resubmit-Job
Client
Printer
Storage
Print
Engine
Process Job
Resubmit-Job (Job A)
Job
A
Job
B
Control Console

## Slide 12: U5: Print a Saved Job via Control Console
Client
Printer
Storage
Print
Engine
Process Job
Job
A
Job
B
Touch, etc. to
select retained job Job A for reprint
Control Console

## Slide 13: IPP Password Protected Job Gaps
JPS2 defined "job-password" and "job-save-disposition" such that they cannot usefully interoperate to support a password protected retained job use case
This use case has been important to some vendors' customers
With IPP's increasing prevalence in the marketplace and its shift in use to more mainstream printing, gaps such as this one should be filled

## Slide 14: U6 : U2/U3 Hybrid - Job Submitted as a Saved Job with Job Password
Printer
Storage
Process Job
Touch, etc. to
enter job password
Control Console
Wait for password
password
Client
Job Creation operation
with "job-password"
Job
A
Print
Engine
Job
A
"job-password"
inhibits processing,
doesn't prevent
reprinting once
processed and
retained

## Slide 15: IPP Job Print Password
Existing attributes do not satisfy this requirement
"job-password" inadequate because of its semantics
  Explicitly associated with the target Job, but doesn't get copied on Restart/Reprint/Resubmit-Job.
  Inhibits "processing" of the job, regardless of the nature of the processing, so in conflict with "save-disposition" = 'save-only'
"document-password" depends on the document format directly supporting authentication credentials

## Slide 16: What is a "Saved Job", Again?
Saved Job [PWG 5100.11]
  A Saved Job is a Retained Job that the Printer retains indefinitely (until removed by a Delete-Job or Purge-Jobs2 operation) so that a copy of it can be reprinted any time using the Reprocess-Job2 or Resubmit-Job operations, rather than aging the job out after an implementation-defined period.
4.3.1.1 Reprinting using the Reprocess-Job operation
  The Reprocess-Job operation [RFC3998] re-processes a copy of any Retained Job after processing was completed, canceled, or aborted. In order to prevent the Printer from aging out a Retained Job, the client can supply a “job-save-disposition” Job Template attribute (see section 7.9) in a job submission. In this case the Printer retains the job (until removed by a Delete-Job or Purge-Jobs operation ) as a Saved Job, so that a client can reprint the job using Reprocess-Job any time subsequently.
4.3.1.2 Reprinting using the Resubmit-Job operation
  The Resubmit-Job operation (see section 5.4 below for a complete description) re-processes a copy of any Retained Job in the same way as Reprocess-Job (see section 4.3.1.1), with the addition of being able to supply additional operation and Job Template attributes that will affect the processing of that copy of the job by either override the values of existing attributes or providing additional attributes.
So: sending "job-save-disposition" is what causes the printer to not age out a Retained Job, thus making it a Saved Job

## Slide 17: Well, now I'm not so sure...
7.9 job-save-disposition (collection)
  The OPTIONAL “job-save-disposition” Job Template attribute is used to archive/save the Document Data of a job, such that the job can be re-printed on demand at some undefined time in the future.
Wait...what? What about the "Job Instructions"? How is only saving the document data the same as saving the Job?

## Slide 18: IPP Job Print Password

## Slide 19: IPP Job Print Password
Goal: Define a "print" password for an IPP Job that:
  Causes the Printer to request the matching password whenever the Job is to be printed
  Is retained if and when the Job is copied (e.g. Resubmit-Job, direct control panel interaction)
  Is set at time of original Job creation
  Is not changeable once set
  Is not exposed via any IPP operation response1 or via any non-IPP protocol
  1 Fetch-Job was discussed as an exception to this rule in earlier "job-reprint-password" drafts

## Slide 20: U7: Job Submitted as a Saved Job with Job Print Password
Printer
Storage
Process Job
Client
Job Creation operation
with "job-save-disposition" and "job-print-password" P
Job
A
Job
A
Print
Engine
P
P
Control Console

## Slide 21: U8: Print a Saved Job via IPP Resubmit-Job and Password (1)
Client
Printer
Print
Engine
Storage
Process Job
Resubmit-Job (Job A, P)
Job
A
Job
B
Control Console
P
P
P

## Slide 22: U9: Print a Saved Job via IPP Resubmit-Job and Password (2)
Client
Printer
Print
Engine
Storage
Process Job
Resubmit-Job (Job A)
Job
A
Job
B
Control Console
P
P
P
Touch, etc. to
enter job reprint password P

## Slide 23: U10: Print a Saved Job via Control Console
Client
Printer
Print
Engine
Storage
Process Job
Job
A
Job
B
Touch, etc. to
select saved job Job A for reprint and P to authorize reprint
Control Console
P
P
P

## Slide 24: Use Case Review
U7: Job Submitted as a Saved Job with Job Reprint Password
  "job-reprint-password" is persistent
U8: Print a Password Protected Saved Job via IPP Resubmit-Job and Password (1)
  IPP Resubmit-Job specifies Saved Job to be printed
  IPP Resubmit-Job supplies password matching "job-print-password" to authorize print
U9: Print a Password Protected Saved Job via IPP Resubmit-Job and Password (2)
  IPP Resubmit-Job specifies Saved Job to be printed
  Printer prompts User for password matching "job-print-password" to authorize print
U10: Print a Password Protected Saved Job via Control Console
  Saved Job to be printed selected via console
  Printer prompts user for password matching "job-print-password" to authorize print

## Slide 25: Other Questions / Comments
®

## Slide 26: Backup